## Slide 1: Introduction to Networking
Module 1
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Basic networking concepts
IP and MAC addresses
Traffic types
OSI and TCP/IP models
Cisco Packet Tracer - Introduction

## Slide 3
Basic networking concepts

## Slide 4: What is a computer network?
Multiple computers linked together
Main reason is to share resources

## Slide 5: How did it start?
ARPANET - The Advanced Research Projects Agency NETwork
Established in 1969
It is the first packet switching network which will use TCP/IP
It was designed for scientific purposes and to share computer resources
It did not start as military purpose network and it was not designed to survive a nuclear attack

## Slide 6: Common Types of Computer Networks
Local Area Network (LAN)
Wide Area Network (WAN)
Wireless Local Area Network (WLAN)
Storage Area Network (SAN)
Home Area Network (HAN)

## Slide 7: Local Area Network (LAN)
Connects network devices over a relatively short distance
Very useful for sharing resources such as data storage and printers

## Slide 8: Wide Area Network (WAN)
Connects multiple LANs together
Extends over a large geographical distance
The Internet is the largest WAN spanning the Earth

## Slide 9: Wireless Local Area Network (WLAN)
Links two or more devices using a wireless distribution method
Operates within limited area

## Slide 10: Storage Area Network (SAN)
Provides block-level network access to storage
The OS will see it as a locally attached storage
Common SAN protocols
  FC
  iSCSI
  AoE (ATA over Ethernet)

## Slide 11: Home Area Network (HAN)

## Slide 12: Common Types of Networking Devices
Hub (obsolete, not secure and very slow)
Switch
Router
Modem
Firewall
Bridge (like a Switch, fewer ports)
Repeater (like a Hub, it just amplifies the signal)

## Slide 13: Ethernet Hub
Used to connect multiple network hosts
Works at Layer 1 of the OSI model
Poor security and performance
Obsolete and now replaced by switches

## Slide 14: Ethernet Switch
Provides end user connectivity
More intelligent than a hub
Has a MAC address table
Provides Layer 2 functionality (and optionally L3)
VLANs can be configured

## Slide 15: Router
Sends packets from one network to another
Provides Layer 3 functionality
Uses IP addresses to transfer packets
“Traffic police” - directs the network traffic to different destinations

## Slide 16: Modem
Digital to analog (and vice versa) signal conversion: MOdulation/DEModulation

## Slide 17: Firewall
Monitors the network traffic and makes decisions what to allow and what to block
Protects a computer network from unauthorized access
It may be hardware device, a software, or a combination of the two

## Slide 18: Bridge and repeater
Bridge
Similar to a Switch
Works at Layer 2
Repeater
Similar to a Hub
Works at Layer 1

## Slide 19: Types of Network Topologies
Bus
Star
Ring
Mesh
Tree
Hybrid

## Slide 20: Networks Protocols
Define a common format and set of rules for exchanging messages between network devices
Common protocols:
  HTTP
  FTP
  SMTP
  DNS
  DHCP
  RDP

## Slide 21: Hyper text transfer protocol (HTTP)
Set of rules to transfer files - text, images, sound, video and other multimedia on the World Wide Web
This is how the browsers talk to the web servers

## Slide 22: File Transfer Protocol (FTP)
Transfer files from one computer to another
You can connect anonymously or with username and password

## Slide 23: Simple Mail Transfer Protocol (SMTP)
Can be used for:
  Server-to-server email transport
  Client-to-server email transport

## Slide 24: Domain Name System (DNS)
Translates domain names into IP addresses (and much more)
It is hierarchical and distributed database

## Slide 25: Dynamic Host Configuration Protocol (DHCP)
Allows a computer to get an IP address from a special server
Uses client-server architecture

## Slide 26: Remote Desktop Protocol (RDP)
Provides a graphical interface to connect to another computer over the network
Can also transfer other resources between the local and remote system, like audio, disk drives and clipboard

## Slide 27: Common Types of Media
“X”TP (“something” Twisted Pair). The “twist” idea introduced by Alexander Bell in 1881
Coaxial Cable
Fiber Optic
Wireless

## Slide 28: “X”TP (“something” Twisted Pair)
UTP – Unshielded Twisted Pair
S/UTP – Screened UTP
STP – Shielded Twisted Pair
S/STP - Screened STP

## Slide 29: EIA/TIA Standards
EIA = Electronic Industries Alliance TIA = Telecommunications Industry Association
T568B is most frequently used

## Slide 30: Straight-through Cable
Pin 1  Pin 1
Pin 2  Pin 2, etc.
Most commonly used to connect devices from different types:
  Host to switch
  Switch to router

## Slide 31: Straight-through Cable (2)
A “straight” cable can be either:
  T568B to T568B OR
  T568A to T568A

## Slide 32: Crossover Cable
Pin 1  Pin 3
Pin 2  Pin 6, etc.
Most commonly used to connect two hosts directly

## Slide 33: Crossover Cable (2)
It is T568B from one side and T568A from the other
Used to connect devices from the same type:
  Host to host
  Router to router
  Host to router (yes, no mistake)

## Slide 34: Auto MDI/MDIX
MDI: Medium Dependent Interface – standard wiring for end stations
MDIX: Medium Dependent Interface Crossover - standard wiring for hubs and switches
The good news! Auto MDI/MDIX automatically detects the required cable connection type and configures the connection appropriately

## Slide 35: Console Cable
Used to connect to the console of a networking device (switch, router)
Usually a USB to Serial adapter is also required

## Slide 36
IP and MAC addresses

## Slide 37: IP Addresses
Known as logical address
Can be assigned to network and end devices
Essential part in routing
Four bytes (octets), separated with “ . “ Example: 1.3.2.8

## Slide 38: IP Addresses (2)

## Slide 39: MAC Addresses
Known as physical address
Unique identifier assigned to network interfaces
48 bits or 6 bytes in a hexadecimal format (discussed later in the course)
Can you change it?

## Slide 40: What is a MAC Address Used for?
Host-to-host communication
Device Identification and tracking
Static IP Assignment (Matched MAC -> receive IP)
MAC Address Filtering
MAC Address Authentication (ISPs use it, for example)

## Slide 41: Example of MAC Address
Windows
Linux

## Slide 42: How to Modify a MAC Address in Windows

## Slide 43: How to Modify a MAC Address in Linux
The new MAC address

## Slide 44
Traffic Types

## Slide 45: Types of traffic
Unicast
Broadcast
Multicast
(Anycast)

## Slide 46: Unicast

## Slide 47: Unicast (2)
Single destination identified by a unique address
Used in host-to-host or host-to-server communication

## Slide 48: Broadcast
Send a message to all recipients simultaneously
Used in DHCP, ARP (will be discussed later)

## Slide 49: Multicast
Transmit a single message to a group of recipients
One-to-many or many-to-many distribution
Examples:
  one person is talking on Skype with two other people
  sending e-mail message to a mailing list
  audio/video streaming

## Slide 50: Anycast
Traffic from a single sender is routed to the nearest node in a group of potential receivers
Advantages:
    better speed/performance
    enhanced reliability
Disadvantages:
    more difficult to implement and troubleshoot
    not supported by all protocols

## Slide 51
OSI and TCP/IP models

## Slide 52: OSI Model
OSI = Open Systems Interconnection
Why?
    Organizes the information
    Simplifies learning
    Standards for the vendors
    Easier troubleshooting
Protocol Data Unit (PDU) – different data format at each layer

## Slide 53: Layer 1 - Physical
The first and lowest layer
Transmitting raw bits
Wiring standards
Devices: hubs, repeaters, modems, cabling, connectors
Protocols: USB, Infrared, Bluetooth

## Slide 54: Layer 2 – Data Link
Switching functions
MAC addresses
Devices: switch, bridge, NIC
Protocols: VLAN, ARP, LLDP, CDP, STP

## Slide 55: Layer 3 – Network
Routing functions
IP addresses
Devices: router, L3 switch
Protocols: IP, ICMP (ping), RIP, OSPF, EIGRP, GRE, etc.

## Slide 56: Layer 4 – Transport
Provides “host-to-host communication”
Services:
  connection-oriented vs connection-less
  reliability (ACK, NACK)
  flow control
  multiplexing (port numbers)
Protocols: TCP, UDP

## Slide 57: TCP Three-Way Handshake
This is how TCP creates a connection over an IP network
a.k.a. “SYN, SYN-ACK, ACK” handshake

## Slide 58: TCP/UDP Twitter Joke

## Slide 59: Layer 5 – Session
Opening, closing and managing a session
Services:
    Authentication
    Authorization
    Session restoration
Protocols: PPTP, L2TP, NetBIOS, RPC

## Slide 60: Layer 6 – Presentation
Sometimes called syntax layer
Acts as data translator for the network
Services:
    data conversion
    compression
    encryption/decryption

## Slide 61: Layer 7 – Application
End-user interaction with the network
Protocols: HTTP(s), FTP, SMTP, Telnet, SSH, RDP

## Slide 62: Mnemonics for the OSI Model
  Away
  Pizza
  Sausage
  Throw
  Not
  Do
  Please
  All
  People
  Seem
  To
  Need
  Data
  Processing

## Slide 63: Data Flow in the OSI Model

## Slide 64: Data Flow in the OSI Model (2)

## Slide 65: Encapsulation and decapsulation
Encapsulation
  Each layer adds it own header (and trailer)
  During the process the packet goes down through the layers
Decapsulation
  Each layer removes the corresponding header (and trailer)
  During the process the packet goes up through the layers

## Slide 66: The TCP/IP Model
Four-layer conceptual model similar to the OSI
Known as the Department of Defense (DoD) model
Why two models?
    They were both created independently

## Slide 67: OSI and TCP/IP Models Comparing

## Slide 68
Cisco Packet Tracer - Introduction
DEMO

## Slide 69: Summary
…
…
…
Basic networking concepts
IP and MAC addresses
Traffic types
OSI and TCP/IP models
Cisco Packet Tracer – Introduction

## Slide 71: СофтУни диамантени партньори

## Slide 72: СофтУни диамантени партньори

## Slide 73: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg