## Slide 1: IP Addresses and Host-to-host Communication
Module 2
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Questions
sli.do #NetFund

## Slide 3: Table of Contents
Binary, decimal and hexadecimal numbers
IPv4
Host-to-Host communication
Switch MAC Address table
Command line
Basic connectivity checks
Demo

## Slide 4
Binary, decimal and hexadecimal numbers

## Slide 5: Different numeral systems
Common Numeral Systems in Computer Networking:
Decimal
Binary
Hexadecimal

## Slide 6: Decimal Numeral System
Base of 10
Called decimal or denary
A single digit can be: 0 1 2 3 4 5 6 7 8 9
In this example:
4x103 + 8x102 + 7x101 + 2x100 =
4000 + 800 + 70 + 2

## Slide 7: Binary Numeral System
Base of 2
Used in computers and all computer-based devices
Each digit is referred to as a bit
A single digit (bit) can be either 0 or 1

## Slide 8: Binary joke

## Slide 9: Hexadecimal Numeral System
Base of 16 (made of 16 symbols)
Widely used by programmers and computer designers
Used in MAC and IPv6 addresses
A single digit can be: 0 1 2 3 4 5 6 7 8 9 A B C D E F

## Slide 10: Questions
sli.do #NetFund

## Slide 11
IPv4

## Slide 12: IPv4 Address
Plays important role for device connectivity
It is a 32-bit address
There are 4 294 967 296 IP addresses (232)

## Slide 13: Private IP addresses
Used for addressing internal networks (offices, HQs etc.)
Not routable on the Internet
Can be reused in many networks
Range of private addresses for each class (classes are discussed later)

## Slide 14: Public IP Addresses
Are not reserved for use in private networks
Globally routed between ISP routers
They are unique
Example: 87.20.114.156

## Slide 15: Public vs. private IP addresses
What are they?
When are they used?
Private Address
Public Address

## Slide 16: NAT: Network Address Translation
It is a method of translating one IP address into another
Example : 192.168.17.45 ---> 227.206.89.76
Private
Public

## Slide 17: NAT (2)

## Slide 18: Questions
sli.do #NetFund

## Slide 19: Network masks
Define the border between the network and the hosts part
Segment the network

## Slide 20: Network masks – Example 1
Class A example:
In decimal: 255.0.0.0
Same mask written with prefix: /8
Same mask written in binary:
11111111.00000000.00000000.00000000
One byte full of 1’s. No address space
Three more bytes full of 0’s. This is 224 - 2 or 16 million computers

## Slide 21: Network masks – Example 2
Class B example:
In decimal: 255.255.0.0
Same mask written with prefix: /16
Same mask written in binary:
11111111.11111111.00000000.00000000
Two bytes with 0’s. This is 216 - 2 or 65534 computers

## Slide 22: Network masks – Example 3
Class C example:
In decimal: 255.255.255.0
Same mask written with prefix: /24
Same mask written in binary:
11111111.11111111.11111111.00000000
One byte with 0’s. This is 28 – 2 or 254 computers

## Slide 23: Network masks – another example
Example:
Host IP address is: 192.168.1.8
Subnet mask is: 255.255.255.0
Network part
Host part

## Slide 24: How many IP addresses for the hosts?
To calculate the number of hosts, use the formula where n is the number of bits in the host part
Example: 192.168.1.0 /24 – how many host addresses?
Answer: We have 8 bits in the host part (n), so:
28 – 2 = 254

## Slide 25: The Network and the Broadcast address
Two important and special addresses:
  The network address – first possible address
  The broadcast address – last possible address
These can NOT be assigned to hosts.

## Slide 26: The Network and the Broadcast address (2)
Example:
192.168.1.5 /24
192.168.1.5
255.255.255.0
192.168.1.0 is the network address
192.168.1.255 is the broadcast address

## Slide 27: A quick challenge
10.15.1.0
Is this a valid HOST IP Address?

## Slide 28: A quick challenge (2)
Well…it depends!
Let’s see it with /23 mask. 10.15.1.0 /23 can be presented as:
10.15.00000001.00000000
255.255.11111110.00000000
First 23 bits
So, is it a valid host IP Address in this case?

## Slide 29: A quick challenge (3)
In the example from the previous slide, which is the first and which is the last possible host address for the subnet to which this IP address belongs?
10.15.1.0 /23
10.15.00000001.00000000
255.255.11111110.00000000
10.15.0.0 is the network address
10.15.1.255 is the broadcast address
10.15.0.1 is the first host address
10.15.1.254 is the last host address

## Slide 30: Questions
sli.do #NetFund

## Slide 31: IP Address Classes
IP Address class is determined by the first octet (byte)
Three of them are used for addressing networks

## Slide 32: IP Address Classes (2)
Examples of class A addresses
  10.0.0.1
  127.0.0.1
  0.0.0.0
Examples of Class B addresses
  172.16.67.8
  169.254.x.x
Examples of Class C addresses
  192.168.1.5
  198.51.100.0

## Slide 33: Introduction to VLSM
VLSM: Variable-Length Subnet Masking
Breaks the IP address classes idea
“Subnetting of subnets”

## Slide 34: Introduction to CIDR
Ignores the concept Network Address Classes
Reduces the amount of route advertisements
Without VLSM and CIDR:
10.1.1.0 /24 will be “seen” as 10.0.0.0 /8
(because /8 is default for Class A)
With VLSM and CIDR:
10.1.1.0 /24 is “seen” as it is
(although the mask is NOT the default)

## Slide 35: Reserved/Special IP Addresses
There are some special IP addresses. For example:
    127.0.0.1 /8
  Known as loopback address
  On most computer systems, “localhost” resolves to the IP address 127.0.0.1
    169.254.X.X /16
  When DHCP is not reachable
  Known as APIPA (Microsoft)

## Slide 36: Questions
sli.do #NetFund

## Slide 37
Host-to-host communication

## Slide 38: Four addresses required
There are 4 addresses needed for Ethernet communication:
Source IP | Destination IP
Source MAC | Destination MAC

## Slide 39: ARP: Address Resolution Protocol
Used to find the MAC address of the destination
Uses Broadcast

## Slide 40: Direct communication (without router)
Source and destination MAC addresses are constant
Source and destination IP addresses are constant

## Slide 41: Host-to-Host Communication With Routers
Source and destination MAC addresses are changed at every hop (router)
Source and destination IP addresses are constant (if we do not have NAT)

## Slide 42: Host-to-Host Communication With Routers (2)

## Slide 43: Host-to-Host Communication With Routers (3)
Source and destination MAC addresses are changed at every hop/router

## Slide 44: Questions
sli.do #NetFund

## Slide 45
Switch MAC Address table

## Slide 46: The MAC address table
It is a (dynamic) table that maps MAC addresses to ports
Used to find the proper interface when the switch forwards a packet

## Slide 47: The MAC address table (2)
You can assign MAC Address statically as well
  Pros : It is more secure
  Cons: It is bit slower and harder for sysadmin to assign it manually

## Slide 48: Questions
sli.do #NetFund

## Slide 49
Command line

## Slide 50: Command Line Introduction
Different vendors use different names but the logic is similar
Typical CLI modes:
  Read-only (User)
  Read-write (Privilege)
  Configuration (Global config)
  Sub-configuration

## Slide 51: Command line
type “enable”
type “configure terminal”
Interface, VLAN, routing, etc.
to go back, type “exit”

## Slide 52: Using the Help – “?”
Use the “?” at each level to see the available commands

## Slide 53: Using the Help – “?” (2)
Use the “?” as you type to see:
  how to finish a command
  what is/are the next word in the command

## Slide 54: Using the Help – TAB
Hit the TAB key here to autocomplete “configure”

## Slide 55: Questions
sli.do #NetFund

## Slide 56
Basic connectivity checks

## Slide 57: Basic Connectivity Checks
Ping (Layer 3)
Traceroute (Layer 3)
LLDP (Layer 2)
CDP (Layer 2)

## Slide 58: Ping
Important Layer 3 connectivity check
Must have IP addresses
ICMP echo request and ICMP echo reply
PING (and traceroute)

## Slide 59: Traceroute
Another L3 connectivity check
Uses the TTL (Time to Live) value in the packet
Can determine the number of hops (routers) in the path

## Slide 60: LLDP: Link Layer Discovery Protocol
Who is connected to me?
Works at Layer 2
Must be enabled on both sides
Vendor-neutral
LLDP (and CDP)

## Slide 61: LLDP (2)
Gathered information with LLDP:
System name and description
Port name and description
VLAN name
IP management address
System capabilities (switching, routing, etc.)
MAC/PHY information
MDI power
Link aggregation

## Slide 62: CDP: Cisco Discovery Protocol
Cisco proprietary
Gathers info about other Cisco (CDP) neighbor devices
Operates at L2
Turned on default by all Cisco switches and routers

## Slide 63: Questions
sli.do #NetFund

## Slide 64
Demonstration

## Slide 65: Summary
…
…
…
Binary, decimal and hexadecimal numbers
IPv4
Host-to-Host communication
Switch MAC Address table
Command line
Basic connectivity checks

## Slide 67: СофтУни диамантени партньори

## Slide 68: СофтУни диамантени партньори

## Slide 69: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg