## Slide 1: Course summary
Module 8
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Questions
sli.do #NetFund

## Slide 3: Table of Contents
Introduction to networking
IP addresses and host-to-host communication
Network access, security and VLANS
Layer 2 redundancy – STP
IP services and basic routing
Dynamic routing with OSPF
Practice

## Slide 4
Introduction to networking

## Slide 5: How did it start?
ARPANET - The Advanced Research Projects Agency NETwork
Established in 1969
It is the first packet switching network which will use TCP/IP
It was designed for scientific purposes and to share computer resources
It did not start as military purpose network and it was not designed to survive a nuclear attack

## Slide 6: Common Types of Computer Networks
Local Area Network (LAN)
Wide Area Network (WAN)
Wireless Local Area Network (WLAN)
Storage Area Network (SAN)
Home Area Network (HAN)

## Slide 7: Local Area Network (LAN)
Connects network devices over a relatively short distance
Very useful for sharing resources such as data storage and printers

## Slide 8: Wide Area Network (WAN)
Connects multiple LANs together
Extends over a large geographical distance
The Internet is the largest WAN spanning the Earth

## Slide 9: Common Types of Networking Devices
Hub (obsolete, not secure and very slow)
Switch
Router
Modem
Firewall
Bridge (like a Switch, fewer ports)
Repeater (like a Hub, it just amplifies the signal)

## Slide 10: Networks Protocols
Define a common format and set of rules for exchanging messages between network devices
Common protocols:
  HTTP
  FTP
  SMTP
  DNS
  DHCP
  RDP

## Slide 11: EIA/TIA Standards
EIA = Electronic Industries Alliance TIA = Telecommunications Industry Association
T568B is most frequently used

## Slide 12: Console Cable
Used to connect to the console of a networking device (switch, router)
Usually a USB to Serial adapter is also required

## Slide 13: IP Addresses
Known as logical address
Can be assigned to network and end devices
Essential part in routing
Four bytes (octets), separated with “ . “ Example: 1.3.2.8

## Slide 14: MAC Addresses
Known as physical address
Unique identifier assigned to network interfaces
48 bits or 6 bytes in a hexadecimal format (discussed later in the course)
Can you change it?

## Slide 15: What is a MAC Address Used for?
Host-to-host communication
Device Identification and tracking
Static IP Assignment (Matched MAC -> receive IP)
MAC Address Filtering
MAC Address Authentication (ISPs use it, for example)

## Slide 16: Types of traffic
Unicast
Broadcast
Multicast
(Anycast)

## Slide 17: OSI Model
OSI = Open Systems Interconnection
Why?
    Organizes the information
    Simplifies learning
    Standards for the vendors
    Easier troubleshooting
Protocol Data Unit (PDU) – different data format at each layer

## Slide 18: Data Flow in the OSI Model

## Slide 19: Data Flow in the OSI Model (2)

## Slide 20: OSI and TCP/IP Models Comparing

## Slide 21: Questions
sli.do #NetFund

## Slide 22
IP addresses and host-to-host communication

## Slide 23: Different numeral systems
Common Numeral Systems in Computer Networking:
Decimal
Binary
Hexadecimal

## Slide 24: Decimal Numeral System
Base of 10
Called decimal or denary
A single digit can be: 0 1 2 3 4 5 6 7 8 9
In this example:
4x103 + 8x102 + 7x101 + 2x100 =
4000 + 800 + 70 + 2

## Slide 25: IPv4 Address
Plays important role for device connectivity
It is a 32-bit address
There are 4 294 967 296 IP addresses (232)

## Slide 26: Private IP addresses
Used for addressing internal networks (offices, HQs etc.)
Not routable on the Internet
Can be reused in many networks
Range of private addresses for each class (classes are discussed later)

## Slide 27: NAT – Network address translation

## Slide 28: Network masks
Define the border between the network and the hosts part
Segment the network

## Slide 29: Network masks example
Example:
Host IP address is: 192.168.1.8
Subnet mask is: 255.255.255.0
Network part
Host part

## Slide 30: A quick challenge
10.15.1.0
Is this a valid HOST IP Address?

## Slide 31: A quick challenge (2)
Well…it depends!
Let’s see it with /23 mask. 10.15.1.0 /23 can be presented as:
10.15.00000001.00000000
255.255.11111110.00000000
First 23 bits
So, is it a valid host IP Address in this case?

## Slide 32: A quick challenge (3)
In the example from the previous slide, which is the first and which is the last possible host address for the subnet to which this IP address belongs?
10.15.1.0 /23
10.15.00000001.00000000
255.255.11111110.00000000
10.15.0.0 is the network address
10.15.1.255 is the broadcast address
10.15.0.1 is the first host address
10.15.1.254 is the last host address

## Slide 33: Reserved/Special IP Addresses
There are some special IP addresses. For example:
    127.0.0.1 /8
  Known as loopback address
  On most computer systems, “localhost” resolves to the IP address 127.0.0.1
    169.254.X.X /16
  When DHCP is not reachable
  Known as APIPA (Microsoft)

## Slide 34: Four addresses required
There are 4 addresses needed for Ethernet communication:
Source IP | Destination IP
Source MAC | Destination MAC

## Slide 35: ARP: Address Resolution Protocol
Used to find the MAC address of the destination
Uses Broadcast

## Slide 36: Direct communication (without router)
Source and destination MAC addresses are constant
Source and destination IP addresses are constant

## Slide 37: Host-to-Host Communication With Routers

## Slide 38: Host-to-Host Communication With Routers (2)
Source and destination MAC addresses are changed at every hop/router

## Slide 39: The MAC address table
It is a (dynamic) table that maps MAC addresses to ports
Used to find the proper interface when the switch forwards a packet

## Slide 40: Command Line Introduction
Different vendors use different names but the logic is similar
Typical CLI modes:
  Read-only (User)
  Read-write (Privilege)
  Configuration (Global config)
  Sub-configuration

## Slide 41: Command line
type “enable”
type “configure terminal”
Interface, VLAN, routing, etc.
to go back, type “exit”

## Slide 42: Using the Help – “?”
Use the “?” at each level to see the available commands

## Slide 43: Using the Help – “?” (2)
Use the “?” as you type to see:
  how to finish a command
  what is/are the next word in the command

## Slide 44: Using the Help – TAB
Hit the TAB key here to autocomplete “configure”

## Slide 45: Basic Connectivity Checks
Ping (Layer 3)
Traceroute (Layer 3)
LLDP (Layer 2)
CDP (Layer 2)

## Slide 46: Questions
sli.do #NetFund

## Slide 47
Network access, security and VLANS

## Slide 48: Saving the configuration
The configuration file must be saved to survive reboot
To save the running configuration file (stored in RAM) to the startup configuration file (stored in NVRAM), use either:
    copy run start
    write memory
running config
startup config
configuration
changes

## Slide 49: Loading the configuration
The saved configuration file (startup config file) will go in the RAM (the running config file) when:
  the device is restarted
  a copy start run command is executed
running config
startup config

## Slide 50: Out-of-band vs in-band management
Out-of-band:
    Management traffic uses separate path from the user traffic
    Typical protocol: Console
In-band management
    Management traffic travels the same path as user traffic
    Typical protocols: Telnet, SSH, SNMP, Web

## Slide 51: In-band management
Management session on top of existing data connection
Needs L3 connectivity – IP addresses are required
More convenient to use but not always secure and reliable

## Slide 52: Secure access - best practices
Physically secure the devices
Use SSH instead of Telnet
Use SNMPv3 instead of v1 or v2
Use HTTPS instead of HTTP
Out-of-band management (console) is considered more secure than in-band management
Create strong passwords for each privilege level and method of access (console, VTY)

## Slide 53: Access (untagged) ports
Used to connect to end-user devices
Can be associated with only one VLAN
Uses the “normal” ethernet frame where there is no VLAN information - no VLAN tag

## Slide 54: Trunk (tagged) ports
Used to connect between switches
Can carry information from/to multiple VLANs
Uses the 802.1Q tagged frame

## Slide 55: Tagging between switches
Untagged
VLAN 1
Untagged

## Slide 56: Trunk port details
Uses IEEE 802.1Q tag to identify each frame
A trunk carries multiple tagged VLANs and (maximum) one untagged VLAN
The untagged VLAN on a trunk is called:
    Native VLAN (Cisco)
    PVID (HPE Comware)
    Untagged VLAN (HPE Provision)

## Slide 57: Questions
sli.do #NetFund

## Slide 58
Layer 2 redundancy - Spanning Tree Protocol

## Slide 59: What is the Spanning Tree Protocol?
It addresses a problem which switches can not handle alone: the broadcast storms
Without STP, a L2 loop will:
    Overload the links
    Affect the end devices
    Cause MAC table instability
    …never stop

## Slide 60: What is the Spanning Tree Protocol? (2)
All STP enabled switches “talk” to each other
The management information that they exchange is in the form of BPDUs (Bridge Protocol Data Units)
The goal is to logically block one or more ports to prevent from loops

## Slide 61: The STP algorithm
Elect the Root switch (Root bridge)
    This is the switch with the lowest BID (Bridge ID)
    BID = Switch Priority and MAC
Select the root ports
    They have the best cost (lowest) to the Root
    Selected per switch
Select the designated ports
    They have the best cost (lowest) to the Root
    Selected per segment (connection)
All other ports go to blocking state

## Slide 62: STP tie-breakers
If there is a tie situation - the same path cost via different paths, use the following tie-breakers:
    When selecting Root port or Designated port, chose the neighboring switch which has the lowest Bridge ID
    If the Bridge ID is the same, select the lowest Port ID (PID)
    Port ID = Port priority and port number

## Slide 63: Link costs (path cost)
Higher port speed -> lower cost
The values can be changed by administrator

## Slide 64: STP Priority
A number between 0 and 61440
Must be configured in increments of 4096
Default is 32768 (+ the VLAN ID)
The switch with the lowest priority will become the Root
If equal values -> lowest MAC address wins (BID = Priority and MAC)

## Slide 65: STP Example
Priority 0
Priority 4096
Priority 32768

## Slide 66: Spanning Tree Protocol – Main Flavors
STP - Spanning Tree Protocol, IEEE 802.1D
RSTP - Rapid STP, IEEE 802.1W
MSTP - Multiple STP, IEEE 802.1S (802.1Q-2005)
PVST+ - Per-VLAN STP, Cisco proprietary

## Slide 67: PVST+
Per-VLAN Spanning Tree is Cisco protocol
Why? It has a similar idea as MSTP -
Creates a spanning tree topology separately
PortFast in PVST+ is similar to Edge port in STP/RSTP
to distribute the load
for each VLAN

## Slide 68: PVST+ (2)

## Slide 69: PVST+ (3)
Switch 2
Switch 3
Vlan 1
Vlan 2
Priority: 0
Priority: 4096
Priority: 32768
Priority: 32768
Priority: 0
Priority: 4096
R
R
Switch 1
Vlan 1
Vlan 2
Vlan 1
Vlan 2
port 1
port 2
port 1
port 2
port 1
port 2

## Slide 70: The good and the bad about PVST+
PVST+ advantages:
  triggers STP calculation only if there is a potential loop in a particular VLAN
  detailed “look” of the network – does not block ports when there is no loop on the trunks for a given VLAN
  PVST+ disadvantages
  generates a lot of overhead in the network
  proprietary protocol

## Slide 71: Questions
sli.do #NetFund

## Slide 72
IP services and basic routing

## Slide 73: What is DHCP?
DHCP: Dynamic Host Configuration Protocol
Provides automatic distribution of IP addresses and other networking parameters such as:
    Subnet mask
    Default gateway
    DNS servers
    More…
Industry standard

## Slide 74: DHCP Components
Server
    DHCP scope - range of addresses (pool), lease time, reservations, etc.
    Uses port UDP 67
Client
    Must be configured to use DHCP
    Uses port UDP 68
(Relay agent)
    Used to serve multiple (V)LANs with a single DHCP server

## Slide 75: The DHCP Process
“DORA”
  Discover
  Offer
  Request
  Acknowledge
All messages use broadcast (IPv4)

## Slide 76: DHCP Relay (2)
Scope settings for 192.168.1.0/24
Scope settings for 172.16.23.0/24

## Slide 77: DNS Introduction
DNS: Domain Name System
DNS Usage:
    To translate names to IP addresses
    To translate IP addresses to names
    To find a particular service in the network
*DNS will be discussed in more details in the advanced course

## Slide 78: DNS “A” Records
One of the most commonly used records in DNS
Matches a hostname (or FQDN) to an IP address
Examples:
  pc1 -> 192.168.1.1
  pc2 -> 192.168.1.2
  server -> 192.168.1.100
  www.abv.bg -> 194.153.145.104
*FQDN = Fully Qualified Domain Name

## Slide 79: Switching vs Routing
Switches:
    Use Layer 2 information (MAC addresses)
    Forwarding decisions based on the MAC address tables
    Not scalable for big networks
    Routers:
        Use Layer 3 information (IP addresses)
        Forwarding decisions based on the routing tables
        Scalable for large networks

## Slide 80: The Routing Table
My routing table:
192.168.5.0/24 via 10.1.1.1
172.16.0.0/16 via 10.15.15.1
87.15.23.0/24 via 10.23.23.1
10.1.1.0/24 is local
10.15.15.0/24 is local
10.23.23.0/24 is local
10.1.1.100
10.15.15.100
10.23.23.100

## Slide 81: Default Gateway

## Slide 82: Default Gateway (2)
My routing table:
192.168.5.0/24 is local
10.1.1.0/24 is local
172.16.0.0/16 via 10.1.1.2
87.15.23.0/24 via 10.1.1.2
10.15.15.0/24 via 10.1.1.2
10.23.23.0/24 via 10.1.1.2
OR
192.168.5.0/24 is local
10.1.1.0/24 is local
0.0.0.0/0 via 10.1.1.2 (default gateway)

## Slide 83: The Rule of the Longest Match
192.168.0.0/16 via 10.1.1.1
192.168.5.0/24 via 10.15.15.1
0.0.0.0/0 via 10.23.23.1
How do I reach 192.168.5.3?
How do I reach 192.168.18.7?
How do I reach 85.12.3.42?
Answer: via 10.15.15.1
Answer: via 10.1.1.1
Answer: via 10.23.23.1

## Slide 84: Direct routing

## Slide 85: Inter-VLAN Routing Using the Same Switch

## Slide 86: Inter-VLAN Routing Using External Switch
Trunk ports

## Slide 87: Inter-VLAN Routing Using External Router
Trunk port

## Slide 88: Static Routes
10.1.1.0/24 is local
192.168.1.0/24 is local
192.168.2.0/24 via 192.168.1.2
10.2.2.0/24 via 192.168.1.2
192.168.1.0/24 is local
192.168.2.0/24 is local
10.1.1.0/24 via 192.168.1.1
10.2.2.0/24 via 192.168.2.3
192.168.2.0/24 is local
10.2.2.0/24 is local
10.1.1.0/24 via 192.168.2.2
192.168.1.0/24 via 192.168.2.2

## Slide 89: Questions
sli.do #NetFund

## Slide 90
Dynamic routing with OSPF

## Slide 91: Distance-vector vs link-state protocols
Distance-vector protocols
Link-state protocols

## Slide 92: RIP Metric: hop count
I will use Router1!
I know how to reach Destination!
I know how to reach Destination!
Note: all routers talk RIP

## Slide 93: OSPF Metric: cost
I will use Router3!
slow links
fast links
I know how to reach Destination!
I know how to reach Destination!
Note: all routers talk OSPF

## Slide 94: Multiple protocols in the same network
?
slow links
fast links
Note: all routers talk RIP and OSPF
RIP: I am better to reach Destination!
OSPF: I am better to reach Destination!

## Slide 95: Administrative distance

## Slide 96: Wildcard masks
In the subnet masks, 1 means “do care” and 0 means “don’t care”
Examples:
    192.168.1.0 255.255.255.0 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 255.255.255.255 -> exact IP address
    In the wildcard masks, 0 means “do care” and 1 means “don’t care”
    Examples:
    192.168.1.0 0.0.0.255 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 0.0.0.0 -> exact IP address

## Slide 97: OSPF terms: router ID
I have many names (interfaces), but just call me 2.2.2.2
Hi, 2.2.2.2!
Hi, 2.2.2.2!

## Slide 98: OSPF terms (2)
Autonomous system
ASBR
ABR
ABR
Area 0 = the backbone area

## Slide 99: Wildcard masks
In the subnet masks, 1 means “do care” and 0 means “don’t care”
Examples:
    192.168.1.0 255.255.255.0 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 255.255.255.255 -> exact IP address
    In the wildcard masks, 0 means “do care” and 1 means “don’t care”
    Examples:
    192.168.1.0 0.0.0.255 -> refers to 192.168.1.0 network
    Loopback address: 10.1.1.1 0.0.0.0 -> exact IP address

## Slide 100: The “network” command
R1:
network 10.0.0.0 0.0.0.255
R2:
network 10.0.0.0 0.0.0.255
network 20.0.0.0 0.0.0.255
10.0.0.1
10.0.0.2
20.0.0.1
Hello!
I have network 10!
Hello!
Hello!
…and 20!
I have network 10!
I have network 10 and 20!

## Slide 101: Single area OSPF configuration
Minimum configuration:
  router ospf process_id
  router-id number (optional)
  network A.B.C.D wildcard_mask area number
Example:
  router ospf 1
  router-id 1.1.1.1 (optional)
  network 192.168.1.0 0.0.0.255 area 0
  network 10.0.0.0 0.0.0.255 area 0

## Slide 102: OSPF passive interface
The “network” command advertises the network AND sends hello messages out of the interface
What if there is non-OSPF device on the other end of the link?
    The Hello packets will be useless
    Represents security issues
    One solution: use passive interfaces

## Slide 103: OSPF passive interface (2)
R1:
network 10.0.0.0 0.0.0.255
R2:
network 10.0.0.0 0.0.0.255
network 20.0.0.0 0.0.0.255
10.0.0.1
10.0.0.2
20.0.0.1
Hello!
I have network 10!
Hello!
Hello!
…and 20!
I have network 10!
I have network 10 and 20!
G0/1
passive-interface G0/1

## Slide 104: Questions
sli.do #NetFund

## Slide 105
Practice

## Slide 106
Corporate WEB and DNS Server
g0/1
g0/2
ge1/0/25
ge1/0/27
ge1/0/26
VLAN 5 (guest): 10.5.5.0/24
VLAN 10 (corporate): 10.10.10.0/24
Internet
Fiber optic
fe0/0/0
fe0/0/1
SSID:
NetFund-Corporate
SSID:
NetFund-Guest

## Slide 107: Topology details
DHCP server for both VLANs is the Cisco device
Juniper is making NAT for both VLANs
Device, interface | IP address
Cisco, VLAN 5 | 10.5.5.1
Cisco, VLAN 10 | 10.10.10.1
HP, VLAN 5 | (10.5.5.10)
HP, VLAN 10 | (10.10.10.10)
Corporate server (Web and DNS) | 10.10.10.101
Juniper, VLAN 5 | 10.5.5.100
Juniper, VLAN 10 | 10.10.10.100
Why are the brackets? 

## Slide 108: Questions
sli.do #NetFund

## Slide 109: Summary
…
…
…
1. Introduction to networking
2. IP addresses and host-to-host communication
3. Network access, security and VLANS
4. Layer 2 redundancy – STP
5. IP services and basic routing
6. Dynamic routing with OSPF
7. Practice

## Slide 111: СофтУни диамантени партньори

## Slide 112: СофтУни диамантени партньори

## Slide 113: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg